## Slide 1
Modeling
Regression models:
  GAM (Generalized Additive Models)
    It is a generalized linear model in which the linear response variable depends linearly on unknown smooth functions of some predictor variables
    It deals natively with non-linearities
    Could integrate autoregressive
terms, if needed (GAMAR models)
    Computational time is higher
compared to ordinary linear
regression.

## Slide 2
Modeling
Black-box models:
  Gradient Boosting
    XGBoost for classification
  Random forest
  Neural networks
  Hyperparameters tuning
    High computational time
  Stacked ensembles

## Slide 3
Optimisation
Genetic Algorithm:
  Used to optimise:
    Model parameters (autoregressive orders, low pass filters, harmonics, splines degrees of freedom, balance point temperatures)
    Control scenarios (setpoint temperatures)
  Normally, binary optimization is used
    It discretises the possible solutions to the problem
    Encode-decode representations for float, integer and categorical data
  Major reason: Flexible technique to be used with all kind of modelling algorithms (Regression, black box,...)

## Slide 4
Optimisation
Genetic Algorithm:
  Minimization objective:
    Single-objective
      Simpler, but the optimisation should account for soft-restrictions
    Multi-objective:
      More computational-effort
      Examples:
        Cost and thermal comfort
        Cost and emissions
        Operational cost and
mantainance cost

## Slide 5
Applications
SIM4BLOCKS: Direct load control of heat pumps
P HP = 60 kWe
V= 3,500 l.
33 offices
4 shops
1 local food market

## Slide 6
Applications
SIM4BLOCKS: Direct load control of heat pumps

## Slide 7
Applications
SIM4BLOCKS: Direct load control of heat pumps
Baseline
Optimized
18 % costs saving

## Slide 8
Applications
SIM4BLOCKS: Direct load control of heat pumps
ENERGY FLEXIBILITY MODEL
Regression model to fit:
P activated
(kW)
P baseline forecasting
(kW)
Day ahead electricity
prices (€)

## Slide 9
Applications
SIM4BLOCKS:
ENERGY FLEXIBILITY FUNCTION

## Slide 10: Data-driven model for enhanced Measurement & Verification
Notes: There is a significant limitation to develop data-driven methodologies for prediction and recommendation which is the need to collect relevant data regarding building characteristics and the impact of energy renovation measures.
We could say that compared to the measurement and verification field it is a quite new and immature field, as we will see in the chapter dedicated specifically to the recommendation techniques developed in this thesis.

## Slide 11: Measurement & Verification
The common approach to estimate energy savings is by comparing the energy consumption after the implementation of the EEMs to a baseline that represents what the consumption would have been without these measures (counterfactual).

## Slide 12: Data-driven model for enhanced M&V
Why research in baseline models for Measurement and Verification?
Measuring the absence of consumed energy is not possible, the only way to verify achieved energy efficiency savings is to use counterfactual consumption models.
The accuracy and uncertainty of the savings estimation will depend on the goodness of the consumption models built.
Having more accurate estimations will increase confidence and boost private investments in energy efficiency.
Notes: This is just to remind why do we actually need accurate models for M&V

## Slide 13: Data-driven model for enhanced M&V
Obtaining accurate estimations of the baseline energy consumption of a building is not trivial, since energy consumption time-series are influenced by several factors:
  Weather variables
  Building occupancy patterns
  User behaviour changes
  Major non-routine events (pandemics, natural disasters…)
  The actual effect of the implemented EEMs

## Slide 14: Proposed methodology
The M&V solution proposed is based on a daily baseline model that estimates consumption as the sum of a baseload that depends on the consumption pattern of the day, and several weather related variable terms.
Once the EEM implementation date is marked, the model attempts to quantify the effect of the measure on both the baseload and the weather dependence of the building.
This methodology, together with the estimated savings, also provides users with insights into the energy usage of the analysed building, most notably consumption profiles and temperature dependence.

## Slide 15: Methodology flowchart
Notes: Explain the flowchart, don’t use too much time
We will analyse one by one the techniques used

## Slide 16: Clustering of electricity consumption profiles

## Slide 17: Time-series partitioning according to the EEM implementation date

## Slide 18: Identification of the change-point temperatures
Notes: 3 different buildings

## Slide 19: Energy baseline model (GAM)
Temperature linear terms
Solar radiation and wind speed splines
Measure effect term
Baseload and holiday term
Notes: g(E(Ed) is the estimator of the link function of the consumption.
Gams use inlk funcions, in this case it was a normal distribution
Two linear terms terms depending on heating and cooling temperatures
Two terms describing the GHI and wind speed splines

## Slide 20: Real building nergy baseline example

## Slide 21: Real building savings estimation example

## Slide 22
Thanks for your attention!
Questions?